## Slide 1: Internet 协议栈

## Slide 2
Protocol “Layers”
Networks are complex!
many “pieces”:
  hosts
  routers
  links of various media
  applications
  protocols
  hardware, software
Question:
Is there any hope of organizing structure of network?
Or at least our discussion of networks?

## Slide 3
Organization of air travel
a series of steps
ticket (purchase)
baggage (check)
gates (load)
runway takeoff
airplane routing
ticket (complain)
baggage (claim)
gates (unload)
runway landing
airplane routing
airplane routing

## Slide 4
Layering of airline functionality
ticket (purchase)
baggage (check)
gates (load)
runway (takeoff)
airplane routing
departure
airport
arrival
airport
intermediate air-traffic
control centers
airplane routing
airplane routing
ticket (complain)
baggage (claim
gates (unload)
runway (land)
airplane routing
ticket
baggage
gate
takeoff/landing
airplane routing
Layers: each layer implements a service
  via its own internal-layer actions
  relying on services provided by layer below

## Slide 5
Why layering?
Dealing with complex systems:
explicit structure allows identification, relationship of complex system’s pieces
  layered reference model for discussion
modularization eases maintenance, updating of system
  change of implementation of layer’s service transparent to rest of system
  e.g., change in gate procedure doesn’t affect rest of system
layering considered harmful?

## Slide 6
Internet protocol stack
application: supporting network applications
  FTP, SMTP, HTTP
transport: process-process data transfer
  TCP, UDP
network: routing of datagrams from source to destination
  IP, routing protocols
link: data transfer between neighboring network elements
  PPP, Ethernet
physical: bits “on the wire”
application
transport
network
link
physical

## Slide 7
Protocol Hierarchies
Layers, protocols, and interfaces

## Slide 8
ISO/OSI reference model
presentation: allow applications to interpret meaning of data, e.g., encryption, compression, machine-specific conventions
session: synchronization, checkpointing, recovery of data exchange
Internet stack “missing” these layers!
  these services, if needed, must be implemented in application
  needed?
application
presentation
session
transport
network
link
physical

## Slide 9
A Critique of the OSI Model and
Why OSI did not take over the world
  Bad timing
  Bad technology
  Bad implementations
  Bad politics

## Slide 10
TCP/IP RM

## Slide 11
A Critique of the TCP/IP Reference Model
Problems:
Service, interface, and protocol not distinguished
Not a general model
Host-to-network “layer” not really a layer
No mention of physical and data link layers
Minor protocols deeply entrenched, hard to replace

## Slide 12
Hybrid Model
TCP/IP Model: Five-layer structure
Internet protocol stack
The hybrid reference model to be used in this book.

## Slide 13
The process of data transfer
5
4
3
2
1
5
4
3
2
1
Computer 1
AP2
AP1
Computer 2
pass data to the application layer
add the application head, becomes msg

## Slide 14
5
4
3
2
1
5
4
3
2
1
Computer 1
AP2
AP1
Computer 2
pass the msg to transport layer
add the transport head
The process of data transfer

## Slide 15
5
4
3
2
1
5
4
3
2
1
Computer 1
AP2
AP1
Computer 2
pass the segment to network
add the network head, becomes datagram
The process of data transfer

## Slide 16
5
4
3
2
1
5
4
3
2
1
Computer 1
AP2
AP1
Computer 2
pass the datagram to the data link layer
add the link head and tail, becomes frame
The process of data transfer

## Slide 17
5
4
3
2
1
5
4
3
2
1
Computer 1
AP2
AP1
Computer 2
pass the frame to the physical layer
physical layers passes the bit stream to the media
The process of data transfer

## Slide 18
5
4
3
2
1
5
4
3
2
1
physical media
Computer 1
AP2
AP1
electronic signal is transmitted in physical media
from the sender PHY to the receiver PHY
Computer 2
The process of data transfer

## Slide 19
5
4
3
2
1
5
4
3
2
1
Computer 1
AP2
AP1
Computer 2
the physical layer receives the bit stream,
and hands over frame to the above data link layer
The process of data transfer

## Slide 20
5
4
3
2
1
5
4
3
2
1
Computer 1
AP2
AP1
Computer 2
data link layer picks out the datagram and
hands over to the network layer
The process of data transfer

## Slide 21
5
4
3
2
1
5
4
3
2
1
Computer 1
AP2
AP1
Computer 2
network layer picks out the segment and
hands over to the transport layer
The process of data transfer

## Slide 22
5
4
3
2
1
5
4
3
2
1
Computer 1
AP2
AP1
Computer 2
transport layer picks out the msg and
hands over to the application layer
The process of data transfer

## Slide 23
5
4
3
2
1
5
4
3
2
1
Computer 1
AP2
AP1
Computer 2
application layer picks out the data and
hands over to the application
The process of data transfer

## Slide 24
5
4
3
2
1
5
4
3
2
1
Computer 1
AP2
AP1
Computer 2
I received the data
sent by AP1！
The process of data transfer

## Slide 25
5
4
3
2
1
5
4
3
2
1
Computer 1
AP2
AP1
Computer 2
application data
app head
H5
10100110100101 bit stream 110101110101
application data
H5
application data
H4
H5
application data
H3
H4
H5
application data
H4
trans head
H3
net head
H2
link
head
T2
link
tail
The process of data transfer

## Slide 26
5
4
3
2
1
5
4
3
2
1
Computer 1
AP2
AP1
Computer 2
10100110100101 bit stream 110101110101
After receiving the bit stream, the physical layer
of computer 2 hands it over to the link layer
H2
T2
H3
H4
H5
application data
The process of data transfer

## Slide 27
H3
H4
H5
application data
5
4
3
2
1
5
4
3
2
1
Computer 1
AP2
AP1
Computer 2
After removing the head and tail of the frame, link
Layer hands over the data to the network layer.
H2
T2
H3
H4
H5
application data
The process of data transfer

## Slide 28
H4
H5
application data
H3
H4
H5
application data
5
4
3
2
1
5
4
3
2
1
Computer 1
AP2
AP1
Computer 2
After removing the head, the network layer
hands over the data to the transport layer.
The process of data transfer

## Slide 29
H5
application data
H4
H5
application data
5
4
3
2
1
5
4
3
2
1
Computer 1
AP2
AP1
Computer 2
After removing the head, the transport layer
hands over the data to the application layer.
The process of data transfer

## Slide 30
application data
H5
application data
5
4
3
2
1
5
4
3
2
1
Computer 1
AP2
AP1
Computer 2
After removing the head, the application layer
hands over the data to the application.
The process of data transfer

## Slide 31
5
4
3
2
1
5
4
3
2
1
Computer 1
AP2
AP1
Computer 2
I received the data
sent by AP1！
The process of data transfer

## Slide 32: Encapsulation
source
application
transport
network
link
physical
Ht
Hn
M
segment
Ht
datagram
destination
application
transport
network
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
M
M
network
link
physical
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
Hn
M
Ht
Hn
Hl
M
router
switch
message
M
Ht
M
Hn
frame

## Slide 33
Functions of each layer
physical layer
establish, maintain and release physical connection between two entities of data link layer.
prescribe the electronic parameter of the physical layer.
prescribe the connector
bit
To transfer bit stream

## Slide 34
Functions of each layer
data link
establish, maintain and release data link, show a right link to the network layer
dividing and synchronization of frames
error detection and control
access control
frame
To transfer data from one node to its adjacent node

## Slide 35
Functions of each layer
network
forwarding
datagram
Host-to-host data transmission
routing

## Slide 36
Functions of each layer
transport
provide logical communication between app processes
error control
sequence control
flow control
segment
Process-to-Process (end2end) data transmission

## Slide 37
Functions of each layer
application
provide interface for users
message

## Slide 38
Protocols and networks
Protocols and networks in the TCP/IP model initially.

## Slide 39
Summary
Protocol layers
Service models