## Slide 1: 传输层服务

## Slide 2
Transport services and protocols
provide logical communication between app processes running on different hosts
transport protocols run in end systems
  send side: breaks app messages into segments, passes to network layer
  rcv side: reassembles segments into messages, passes to app layer
more than one transport protocol available to apps
  Internet: TCP and UDP

## Slide 3
Transport vs. network layer
network layer: logical communication between hosts
transport layer: logical communication between processes
  relies on, enhances, network layer services
Household analogy:
12 kids sending letters to 12 kids
processes = kids
app messages = letters in envelopes
hosts = houses
transport protocol = Ann and Bill
network-layer protocol = postal service

## Slide 4
Internet transport-layer protocols
reliable, in-order delivery (TCP)
  congestion control
  flow control
  connection setup
unreliable, unordered delivery: UDP
  no-frills extension of “best-effort” IP
services not available:
  delay guarantees
  bandwidth guarantees

## Slide 5
Internet transport-layer protocols

## Slide 6
Summary
Transport services
Internet transport-layer protocols