## Slide 1: TCP报文段格式

## Slide 2
TCP: Overview RFCs: 793, 1122, 1323, 2018, 2581
point-to-point:
  one sender, one receiver
reliable, in-order byte steam:
  no “message boundaries”
pipelined:
  TCP congestion and flow control set window size
send & receive buffers
full duplex data:
  bi-directional data flow in same connection
  MSS: maximum segment size
connection-oriented:
  handshaking (exchange of control msgs) init’s sender, receiver state before data exchange
flow controlled:
  sender will not overwhelm receiver

## Slide 3
TCP segment structure

## Slide 4
TCP segment structure - Control field

## Slide 5
TCP segment structure

## Slide 6
TCP seq. #’s and ACKs
Seq. #’s:
  byte stream “number” of first byte in segment’s data
ACKs:
  seq # of next byte expected from other side
  cumulative ACK
Q: how receiver handles out-of-order segments
  A: TCP spec doesn’t say, - up to implementor

## Slide 7
TCP seq. #’s and ACKs
User
types
‘C’
host ACKs
receipt
of echoed
‘C’
host ACKs
receipt of
‘C’, echoes
back ‘C’
simple telnet scenario
Host B
Host A
seq=42, ack=79, data = ‘C’
seq=79, ack=43, data = ‘C’
seq=43, ack=80

## Slide 8
Summary
TCP segment structure
TCP seq. # and ACK #