## Slide 1: 广播

## Slide 2
Broadcast Routing
deliver packets from source to all other nodes
source duplication is inefficient:
source duplication: how does source determine recipient addresses?

## Slide 3
In-network duplication
flooding: when node receives brdcst pckt, sends copy to all neighbors
  Problems: cycles & broadcast storm
controlled flooding: node only brdcsts pkt if it hasn’t brdcst same packet before
  Node keeps track of pckt ids already brdcsted
  Or reverse path forwarding (RPF): only forward pckt if it arrived on shortest path between node and source
spanning tree
  No redundant packets received by any node

## Slide 4
Spanning Tree
First construct a spanning tree
Nodes forward copies only along spanning tree

## Slide 5
Spanning Tree: Creation
Center node
Each node sends unicast join message to center node
  Message forwarded until it arrives at a node already belonging to spanning tree
A
B
G
D
E
c
F
1
2
3
4
5
Stepwise construction of spanning tree
A
B
G
D
E
c
F
(b) Constructed spanning tree

## Slide 6
Summary
Broadcast Routing
Spanning Tree