## Slide 1: 差错检测与纠错

## Slide 2
Error Detection
EDC = Error Detection and Correction bits (redundancy)
D = Data protected by error checking, may include header fields
Error detection not 100% reliable!
  protocol may miss some errors, but rarely
  larger EDC field yields better detection and correction

## Slide 3
Parity Checking
Single Bit Parity:
Detect single bit errors
Two Dimensional Bit Parity:
Detect and correct single bit errors

## Slide 4
Internet checksum (review)
Sender:
treat segment contents as sequence of 16-bit integers
checksum: addition (1’s complement sum) of segment contents
sender puts checksum value into UDP checksum field
Receiver:
compute checksum of received segment
check if computed checksum equals checksum field value:
  NO - error detected
  YES - no error detected. But maybe errors nonetheless?
Goal: detect “errors” (e.g., flipped bits) in transmitted packet (note: used at transport layer only)

## Slide 5
Checksumming: Cyclic Redundancy Check
view data bits, D, as a binary number
choose r+1 bit pattern (generator), G
goal: choose r CRC bits, R, such that
  <D,R> exactly divisible by G (modulo 2)
  receiver knows G, divides <D,R> by G. If non-zero remainder: error detected!
  can detect all burst errors less than r+1 bits
widely used in practice (Ethernet, 802.11 WiFi, ATM)

## Slide 6
CRC Example
Want:
  D.2r XOR R = nG
equivalently:
  D.2r = nG XOR R
equivalently:
if we divide D.2r by G, want remainder R
R = remainder[ ]
D.2r
G

## Slide 7
Summary
Parity Checking
CRC