## Slide 1: 信道分割式MAC协议

## Slide 2
MAC Protocols: a taxonomy
Three broad classes:
Channel Partitioning
  divide channel into smaller “pieces” (time slots, frequency, code)
  allocate piece to node for exclusive use
Random Access
  channel not divided, allow collisions
  “recover” from collisions
“Taking turns”
  nodes take turns, but nodes with more to send can take longer turns

## Slide 3
Channel Partitioning MAC protocols: TDMA
TDMA: time division multiple access
access to channel in "rounds"
each station gets fixed length slot (length = pkt trans time) in each round
unused slots go idle
example: 6-station LAN, 1,3,4 have pkt, slots 2,5,6 idle

## Slide 4
Channel Partitioning MAC protocols: FDMA
FDMA: frequency division multiple access
channel spectrum divided into frequency bands
each station assigned fixed frequency band
unused transmission time in frequency bands go idle
example: 6-station LAN, 1,3,4 have pkt, frequency bands 2,5,6 idle

## Slide 5
Summary
TDMA
FDMA