## Slide 1: 以太网

## Slide 2
Ethernet
History
  Developed by Bob Metcalfe and others at Xerox PARC in mid-1970s
  Roots in Aloha packet-radio network
  Standardized by Xerox, DEC, and Intel in 1978
  LAN standards define MAC and physical layer connectivity
    IEEE 802.3 (CSMA/CD - Ethernet) standard – originally 2Mbps
    IEEE 802.3u standard for 100Mbps Ethernet
    IEEE 802.3z standard for 1,000Mbps Ethernet
CSMA/CD: Ethernet’s Media Access Control (MAC) policy
  CS = carrier sense
    Send only if medium is idle
  MA = multiple access
  CD = collision detection
    Stop sending immediately if collision is detected

## Slide 3
Ethernet
“dominant” wired LAN technology:
cheap $20 for NIC
first widely used LAN technology
simpler, cheaper than token LANs and ATM
kept up with speed race: 10 Mbps – 10 Gbps
Metcalfe’s Ethernet
sketch

## Slide 4
Ethernet Frame Structure
Sending adapter encapsulates IP datagram (or other network layer protocol packet) in Ethernet frame
Preamble:
7 bytes with pattern 10101010 followed by one byte with pattern 10101011
used to synchronize receiver, sender clock rates

## Slide 5
Ethernet Frame Structure (more)
Addresses: 6 bytes
  if adapter receives frame with matching destination address, or with broadcast address (eg ARP packet), it passes data in frame to network layer protocol
  otherwise, adapter discards frame
Type: indicates higher layer protocol (mostly IP but others possible, e.g., Novell IPX, AppleTalk)
CRC: checked at receiver, if error is detected, frame is dropped

## Slide 6
Ethernet uses CSMA/CD
No slots
adapter doesn’t transmit if it senses that some other adapter is transmitting, that is, carrier sense
transmitting adapter aborts when it senses that another adapter is transmitting, that is, collision detection
Before attempting a retransmission, adapter waits a random time, that is, random access

## Slide 7
Ethernet CSMA/CD algorithm
1. NIC receives datagram from network layer, creates frame
2. If NIC senses channel idle, starts frame transmission If NIC senses channel busy, waits until channel idle, then transmits
3. If NIC transmits entire frame without detecting another transmission, NIC is done with frame !
4. If NIC detects another transmission while transmitting, aborts and sends jam signal
5. After aborting, NIC enters exponential backoff: after mth collision, NIC chooses K at random from {0,1,2,…,2m-1}. NIC waits K·512 bit times, returns to Step 2

## Slide 8
Exponential Backoff
If a collision is detected, delay and try again
Delay time is selected using binary exponential backoff
  1st time: choose K from {0,1} then delay = K * 51.2us
  2nd time: choose K from {0,1,2,3} then delay = K * 51.2us
  nth time: delay = K x 51.2us, for K=0..2n – 1
    Note max value for k = 1023
  give up after several tries (usually 16)
    Report transmit error to host
If delay were not random, then there is a chance that sources would retransmit in lock step
Why not just choose from small set for K
  This works fine for a small number of hosts
  Large number of nodes would result in more collisions

## Slide 9
State Diagram for CSMA/CD

## Slide 10
CSMA/CD efficiency
Tprop = max prop delay between 2 nodes in LAN
ttrans = time to transmit max-size frame
efficiency goes to 1
  as tprop goes to 0
  as ttrans goes to infinity
better performance than ALOHA: and simple, cheap, decentralized!

## Slide 11
Ethernet Performance
Efficiency of Ethernet at 10 Mbps with 512-bit slot times.

## Slide 12
802.3 Ethernet Standards: Link & Physical Layers
many different Ethernet standards
  common MAC protocol and frame format
  different speeds: 2 Mbps, 10 Mbps, 100 Mbps, 1Gbps, 10G bps
  different physical layer media: fiber, cable
application
transport
network
link
physical
MAC protocol
and frame format
100BASE-TX
100BASE-T4
100BASE-FX
100BASE-T2
100BASE-SX
100BASE-BX
fiber physical layer
copper (twister
pair) physical layer

## Slide 13
Ethernet Cabling
The most common kinds of Ethernet cabling.

## Slide 14
Ethernet Problems
Ethernet’s peak utilization is pretty low (like Aloha)
Peak throughput worst with
  More hosts
    More collisions needed to identify single sender
  Smaller packet sizes
    More frequent arbitration
  Longer links
    Collisions take longer to observe, more wasted bandwidth
  Efficiency is improved by avoiding these conditions

## Slide 15
Summary
Ethernet