## Slide 1: 交换机

## Slide 2
Switch
link-layer device: smarter than hubs, take active role
  store, forward Ethernet frames
  examine incoming frame’s MAC address, selectively forward frame to one-or-more outgoing links when frame is to be forwarded on segment, uses CSMA/CD to access segment
transparent
  hosts are unaware of presence of switches
plug-and-play, self-learning
  switches do not need to be configured

## Slide 3
Switch: allows multiple simultaneous transmissions
hosts have dedicated, direct connection to switch
switches buffer packets
Ethernet protocol used on each incoming link, but no collisions; full duplex
  each link is its own collision domain
switching: A-to-A’ and B-to-B’ simultaneously, without collisions
  not possible with dumb hub
switch with six interfaces
(1,2,3,4,5,6)

## Slide 4
Switch Table
Q: how does switch know that A’ reachable via interface 4, B’ reachable via interface 5?
A: each switch has a switch table, each entry:
  (MAC address of host, interface to reach host, time stamp)
looks like a routing table!
Q: how are entries created, maintained in switch table?
  something like a routing protocol?
switch with six interfaces
(1,2,3,4,5,6)

## Slide 5
Switch: self-learning
switch learns which hosts can be reached through which interfaces
  when frame received, switch “learns” location of sender: incoming LAN segment
  records sender/location pair in switch table
A
B
C
C’
1
2
3
4
5
6
A A’
Source: A
Dest: A’
MAC addr interface TTL
Switch table
(initially empty)
A
1
60

## Slide 6
Switch: frame filtering/forwarding
When frame received:
1. record link associated with sending host
2. index switch table using MAC dest address
3. if entry found for destination then {
if dest on segment from which frame arrived then drop the frame
else forward the frame on interface indicated
}
else flood
forward on all but the interface
on which the frame arrived

## Slide 7
Self-learning, forwarding: example
A
A’
B
B’
C
C’
1
2
3
4
5
6
A A’
Source: A
Dest: A’
A A’
A A’
A A’
A A’
A A’
A’ A
frame destination unknown:
flood
destination A location known:
selective send
MAC addr interface TTL
Switch table
(initially empty)
A
1
60
A’
4
60

## Slide 8
Interconnecting switches
switches can be connected together
Q: sending from A to G - how does S1 know to forward frame destined to F via S4 and S3?
A: self learning! (works exactly the same as in single-switch case!)
A
B
S1
C
D
E
F
S2
S4
S3
H
I
G

## Slide 9
Switch: traffic isolation
switch installation breaks subnet into LAN segments
switch filters packets:
  same-LAN-segment frames not usually forwarded onto other LAN segments
  segments become separate collision domains

## Slide 10
Institutional network

## Slide 11
Switches vs. Routers
both store-and-forward devices
  routers: network layer devices (examine network layer headers)
  switches are link layer devices
routers maintain routing tables, implement routing algorithms
switches maintain switch tables, implement filtering, learning algorithms

## Slide 12
Summary
Switch